## Slide 1
MOBILITY MODELS IN MOBILE COMPUTING
Understanding how mobile users and devices move through an environment
Name: Ajay. P
Register No: 1972260095

## Slide 2
What Is a Mobility Model?
02 • MOBILE COMPUTING
A mobility model describes how a mobile user or device moves over time.
It can define movement direction, speed, pause time and destination.
Researchers use models to imitate realistic movement in a computer simulation.
Examples of mobile entities: smartphones, vehicles, robots and wireless sensor nodes.
Movement
Where does the device go?
Speed
How fast does it move?
Pause time
Does it stop before moving again?

## Slide 3
Why Are Mobility Models Needed?
03 • MOBILE COMPUTING
Network testing
Test wireless network performance under movement.
Protocol design
Evaluate routing and handoff methods.
Cost saving
Simulate scenarios before real-world deployment.
Performance measures
Study delay, packet loss and throughput.
Coverage planning
Understand changing connections as users move.

## Slide 4
Main Categories of Mobility Models
04 • MOBILE COMPUTING
Entity-based models
Describe movement of individual users or devices. Examples: Random Waypoint, Random Walk and Gauss–Markov.
Group-based models
Describe people or devices moving together or following a leader. Examples: Reference Point Group Mobility and group movement in a crowd.
The best model depends on the real situation being simulated.

## Slide 5
Random Walk Mobility Model
05 • MOBILE COMPUTING
The device chooses a random direction and speed for each movement step.
After a step, it chooses another direction and continues.
Movement is unpredictable and does not require a fixed destination.
Useful for simple simulations, but may not represent real human travel well.
Example path
Each turn is chosen randomly.

## Slide 6
Random Waypoint Mobility Model
06 • MOBILE COMPUTING
A device selects a random destination within a defined area.
It travels toward that destination at a chosen speed.
It may pause for a set time after reaching the destination.
Then it selects another destination and repeats the process.
1. Choose
Pick a random point.
2. Move
Travel toward the point.
3. Pause
Wait, then choose again.
Example: a person walking between different places on a campus.

## Slide 7
Gauss–Markov Mobility Model
07 • MOBILE COMPUTING
Movement is smoother because the next speed and direction depend partly on the previous ones.
A tunable parameter controls how much movement is predictable versus random.
It avoids some of the sudden turns seen in basic random models.
Useful for modeling vehicles or users whose movement changes gradually.
Previous movement
Influences the next step.
Small changes
Speed and direction can change gradually.
Result
A smoother path.

## Slide 8
Group Mobility Models
08 • MOBILE COMPUTING
A group of mobile users moves together or maintains relationships while moving.
Some models use a leader or reference point to guide the group.
Members may move around the group’s general direction rather than follow identical paths.
Examples: friends walking together, a tour group or soldiers moving as a unit.
Group movement illustration
Leader
Members follow the group's general movement.

## Slide 9
Vehicular and Road-Based Mobility
09 • MOBILE COMPUTING
Vehicles usually move along roads instead of choosing any point in an open area.
Movement depends on road layout, speed limits, traffic signals and congestion.
Vehicles may slow down, stop and turn at intersections.
Used to simulate vehicular ad hoc networks (VANETs), smart traffic and connected cars.
Road-constrained movement

## Slide 10
Comparison of Common Mobility Models
10 • MOBILE COMPUTING
Model | Movement pattern | Typical use
Random Walk | Random step-by-step direction | Basic mobility tests
Random Waypoint | Random destination + possible pause | General mobile users
Gauss–Markov | Gradual changes in speed/direction | Smoother movement
Group Mobility | Users move as a group | Crowds or teams
Road-Based | Movement follows roads and traffic | Vehicles and VANETs
No single model is best for every scenario.

## Slide 11
SUMMARY & THANK YOU
Mobility models represent how devices and users move over time.
They help researchers test wireless networks and communication protocols.
Common models include Random Walk, Random Waypoint, Gauss–Markov, group and road-based models.
Choose a model that matches the real environment being studied.
THANK YOU